## Slide 1: Archdiocese of Seattle
CHURCH VOTIVE CANDLES
SAFETY ALERT

## Slide 2: CHURCH VOTIVE CANDLES
These come in all sizes
SMALL

## Slide 3: CHURCH VOTIVE CANDLES
These come in all sizes
MEDIUM

## Slide 4: CHURCH VOTIVE CANDLES
These come in all sizes
LARGE

## Slide 5: SERIES OF EVENTS
Mass concludes in the evening
Small votive holder fails and fire falls to the carpeted floor
Fire ignites surrounding flooring/area

## Slide 6: FIRE EVENT

## Slide 7: SERIES OF EVENTS
Fire self extinguishes sometime overnight
12 hours later, Church reopen & staff notices fire
Industrial hygienist is dispatched with clean up contractor. Original plan was smoke/soot clean up.

## Slide 8: CONSEQUENCES
Initial reserve estimate for cleaning <$100,000
Smoke/Soot entered HVAC System – System Cleaned
Smoke/Soot damaged carpeting – Entire Church carpet replaced

## Slide 9: CONSEQUENCES
Walls cannot be cleaned – Substantial interior repainting
Claim grows to $300,000
CCAS self insured to $250,000. Excess covered by carrier

## Slide 10: COMBUSTABLE STATUE BASE

## Slide 11: FAILED VOTIVE CANDLE HOLDER

## Slide 12: COMUBUSTABLE CARPET BELOW HOLDER

## Slide 13: REMEDIES
1. If votive candle stands are used, noncombustible material such as tile, stone, marble, or granite should be in place beneath the candle lighting/burning area. If candle stands are positioned over carpet, provide a fire resistant mat or Plexiglas sheet under the stands to reduce fire as well as protect the surface underneath from damage due to dropped matches or spilled candle wax.

## Slide 14: REMEDIES
2. Do not allow candles to be brought into church from parishioners or visitors. Only allow parish candles purchased by a reputable candle manufacturer to be displayed and lit. Many of the candles purchased at discount stores are improperly made and have been the source of numerous fires.

## Slide 15: REMEDIES
3. Keep candles away from combustible items such as linens, runners, or curtains. Even flowers placed too close to a flame can ignite when they become dry.
4. Keep candles and all open flames away from flammable liquids.

## Slide 16: REMEDIES
5. Candles should be placed in double-insulated containers or secured by a sturdy non-combustible base/holder.
6. Care must be taken in the placement of candles in relation to seating, foot traffic areas, and exits.

## Slide 17: REMEDIES
7. Keep candles free of foreign objects such as matches and wick clippings.
8. Ensure matches, lighting sticks and lighters are safely out of the reach of children.

## Slide 18: REMEDIES
9. Provide a noncombustible container filled with sand to extinguish and place matches or lighting sticks.

## Slide 19: REMEDIES
10. Discourage the use of candles in schools and all offices. The only exception should be for religious/prayer purposes in a classroom, but the candle must be extinguished immediately when concluded.

## Slide 20: REMEDIES
11. Keep wicks trimmed to one-quarter inch and extinguish them when they get to within two inches of the holder. Candles should be extinguished before the last half-inch of wax begins to melt.

## Slide 21: REMEDIES
12. Extinguish candles with a snuffer, avoiding burns from hot wax.
13. Let candles and holders cool sufficiently prior to moving.

## Slide 22: REMEDIES
14. Never leave a candle burning in an unoccupied room. The only exceptions would be for votive candles or the sanctuary lamp candle. These candles are specifically manufactured to burn until they self-extinguish.

## Slide 23: REMEDIES
15. Never let candles burn for more than four hours at a time. The same exceptions as above would apply.
16. The flame of a candle should not be closer than three inches to other candle flames.

## Slide 24: REMEDIES
17. No lit candles on live or artificial holiday greenery. Exception: Any artificial wreath (i.e. advent wreath must be fire retardant treated and candles set in protective container).

## Slide 25: REMEDIES
18. Ensure a 5 pound ABC dry chemical fire extinguisher is wall mounted near the location of candles.